United States Department of Agriculture

Natural Resources Conservation Service

Instructions for Digitizing and Transmitting Easement Boundaries to the Geospatial Enterprise Operations Branch (GEO), Fort Worth, TX

December 2021 – Current updates to these instructions will be included with the Easement checkout email notifications.

Geospatial Enterprise Operations Branch

(Fort Worth, TX)

Sponsor:

Carrie Lindig, Director, Easements Program Division (EPD)

Easement Programs Division

USDA Natural Resources Conservation Service 1400 Independence Avenue, SW

Washington, D.C.

20250

Contact:

Lori Uhlhorn, Geospatial Data Management and Provisioning Section Chief

Geospatial Enterprise Operations Branch (GEO)

Farm Production and Conservation Business Center

U.S. Department of Agriculture

125 S. State St.,Ste. 6416

Salt Lake City UT 84138 801-844-2903

Technical Contacts:

Steven Nechero, Geospatial Services Team Lead

Geospatial Enterprise Operations Branch (GEO)

Farm Production and Conservation Business Center

U.S. Department of Agriculture

501 W. Felix St., Bldg. 23

Fort Worth, Texas 76115 817-509-3366

Laura Davenport-Wade, Cartographer

Geospatial Enterprise Operations Branch (GEO)

Farm Production and Conservation Business Center

U.S. Department of Agriculture

501 W. Felix St., Bldg. 23

Fort Worth, Texas 76115 817-509-3379

Table of Contents

Background	1

NEST Checkout Data Generation Process	1

Check Out Data Structure	2

Process	3

Attribute the Easement	4

Topology Check	4

Additional Training Materials	5

ESRI Virtual Campus	5

# Background

The National Easements Geodatabase (NEG) contains the digitized boundaries of all NRCS easement stewardship lands in a seamless national layer. The National Easement Staging Tool (NEST), the official agency database for easement programs, contains the attributes of the easement parcel, and its associated program stored in the tabular database as a point record. The majority of the attributes of the NEG polygons are adopted from their corresponding NEST points through a spatial join process. The few remaining attributes must be entered by the State Geographic Information System (GIS) user.

The NEST attributes are extracted, created into points, and provided as READ ONLY. No changes made to the NEST attributes will post back to the NEST database. Changes needed to the NEST portions of the records must be made in the NEST system by the approved NEST State contact.

Transmitting the digitized boundaries of stewardship easements involves a matching process between the newly submitted NEG spatial boundaries and their associated NEST points. The tools that were previously used are to complete the spatial join and Quality Assurance (QA) process are no longer supported at NGCE. The NEST point QA check is being conducted by NPAD after check-in of boundary data.

For more information, please refer to Manual 440, Part 528 – Agriculture Conservation Easement Program located at https://directives.sc.egov.usda.gov/viewDirective.aspx?hid=36843

To use this process, you must use ArcGIS 10.2 or greater, but editing in ArcGIS Pro is also allowed.

# NEST Checkout Data Generation Process

The checkouts are generated quarterly based upon the fiscal year. The annual schedule is as follows:

| Quarter | Date Range | Checkouts Available | Check-in Due |
| --- | --- | --- | --- |
| 1 | October 1 thru December 31 | November 1 | January 1 |
| 2 | January 1 thru March 31 | February 1 | April 1 |
| 3 | April 1 thru June 30 | May 1 | July 1 |
| Q4 (Flight Planning deadline) | July 1 thru August 20 | August 1 | August 20 for Flight Planning |
| or Q4 (Quarter End deadline) | July 1 thru September 30 | August 1 | October 1 |

Early in each quarter, NEST matching geodatabase checkouts for each State will become available. The geodatabase MUST be returned at the close of the quarter if updates have been made. The data sets expire at the end of the quarter as shown in the checkout due date field of the Easements_a_Matched feature class. Only the boundaries that have an existing matched NEST point can be submitted.

The checkouts are generated by state using the “Admin_Area” field of the easements and the “NEST_STATE” field of the NEST points. The points are extracted along with the easements for that State and other base layers utilized in the checkout process into a file geodatabase.

# Check Out Data Structure

Each State will receive a new checkout from the Fort Worth Geospatial Enterprise Operations Branch (GEO) for the current quarter.

The checkout contains a directory by state abbreviation ([ST]), two file geodatabases (Ease_A.gdb and ReturnToGEO.gdb), an ArcMap document file (EaseChkOut.mxd), and an instruction document (Instructions for Digitizing and Transmitting Easement Boundaries to the Geospatial Enterprise Operations Branch (GEO), Fort Worth, TX).

The checkout geodatabase (Ease_A.gdb) contains one feature dataset (FDS), also called Ease_A. The Ease_A FDS contains only matched polygons as the Easements_a_Matched and NonSteward_Matched layers . These layers represent the production version of the NEST data.

Remember that only the boundaries that match the NEST points can be submitted.

Below are the Ease_A FDS data layer descriptions (the ReturnToGEO.gdb Ease_A FDS also contains these same layers, but they are empty layers so that you can add only the new/updated/changed polygons or moved NEST points for return to the Fort Worth GEO office).

|  |  | Stewardship layer that you digitize, copy, or paste easements into (NEST matched only). |
| --- | --- | --- |
|  |  | Stewardship layer that you digitize, copy, or paste easements into (no NEST point exists to date). |
|  |  | Non-Stewardship layer that you digitize, copy, or paste easements into (NEST matched only). |
|  |  | Non-Stewardship layer that you digitize, copy, or paste easements into (no NEST point exists to date). |
|  |  | Stewardship NEST points. |
|  |  | Non-Stewardship NEST points. |

The Nest_Ease_a_ALL file contains all of the NEST points in your state. If your NEST Point is outside of the boundary that it matches, and you are certain the boundary is accurate, simply use your ArcMap editing tools to move the point to the polygon center.

All polygons need to be matched to a single NEST point. A polygon may be a single or multipart polygon. A multipart polygon is always defined by a single data row. If you have 2 component parts, please merge them into a single multipart polygon before matching. If you have two records for an easement due to a contract conversion, please match the newest record and move the old record outside of the boundary. You are not re-matching already matched records. Add your new polygons to the Easements_A_Matched layer and drag your points within the corresponding polygons where needed until you have all polygons loaded and containing a single point.

# Process

- Copy the Checkout directory [ST] to any location on your local drive.

- In ArcMap, open the .mxd provided with your checkout.

- Start an edit session by clicking Editor>Start Editing on the Editor toolbar.

- Add the easement boundary to the Ease_a_Matched layer by importing, appending, copy/pasting. Notes:

  - Make sure you handle any necessary coordinate system reprojections before adding the boundary to this table. You should resolve the datum and coordinate system to the Datum: D_WGS_1984; Geographic Coordinate System: GCS_WGS_1984.

  - The boundary must contain the NEST point it represents, adjust the NEST point to fall within the boundary. You must have a one-point-to-one-polygon relationship in order to match.

- Stop the edit session and Save your edits.

## Attribute the Easement

- Open the Ease_a_Matched and the Nest_Ease_a_All attribute tables. Tile the tables so both are viewable.

- Start an edit session to edit the Ease_a_Matched attribute table.

- Use the Select features	tool located on the Tools toolbar and select the NEST point and easement boundary simultaneously.

- Scroll to the new easement located at the bottom of the table.

- Enter the attributes in the format of the attributes. Use the attributes of existing boundaries as a guide.

| Admin_Area | Enter the state abbreviation. |
| --- | --- |
| New_Agree_Num | The NEST_Agreement number from the Nest_Ease_a_ALL file . |
| 2021 Methods | Definition | Supporting Information |
| NEW SURVEYS and RE-ESABLISHMENT SURVEYS |
| Legal Survey - Survey Grade GPS or State Plane Coordinates | The parcel’s boundary has been constructed from coordinate geometry sourced from a modern Legal Survey plat which uses survey-grade GPS as its basis of bearing and geographic positioning. | For new and re-established easement surveys from a Licensed Professional Surveyor. A reference in the comments section should be made as to the type of GPS observations taken (e.g., type of survey grade GPS and datum). |
| EASEMENT BOUNDARY CORRECTIONS |
| Legal Survey - Georeferenced/COGO | The parcel’s boundary has been constructed from coordinate geometry (COGO) sourced from a Legal Survey plat using the associated Geographic Position (GP) 2 data or a known published station to position the parcel. | For older surveys that have known coordinates. The vintage or currency of the survey and the associated GP or published station should be provided in the comments section. |
| Legal Survey - Georeferenced/COGO from Shared Data/Alternate Source3 | The parcel’s boundary has been constructed from coordinate geometry sourced from a Legal Survey plat and positioned using GP data from adjacent or related surveys. Shared data may include City, County, State, Federal and Alternate Commercial sources. | A reference in the comments section should be made to the adjacent or related surveys used in positioning. |
| Legal Survey – Natural or ROW Feature Georeferenced/COGO | The parcel’s boundary has been constructed from coordinate geometry using a legal survey. Georeferencing and rotation of the easement boundary is based on natural features from imagery. (navigable water body, roadway, mountain ridge, ROW, canal, etc. | The vintage or currency of the imagery should be provided in the comments section. |
| Recorded WED - Georeferenced/COGO | The parcel’s boundary is constructed from information sourced from recorded easement deed and geographically positioned using GP data and information sourced from the same record. | The vintage or currency of the geographic position should be provided in the comments section. |
| Recorded WED – Natural or ROW Feature Georeferenced/COGO | The parcel’s boundary has been constructed from information sourced from a recorded easement deed. Georeferencing and rotation COGO from aliquot description or metes and bounds of the easement boundary is based on natural features from imagery. (navigable water body, roadway, mountain ridge, ROW, canal, etc. | The vintage or currency of the imagery should be provided in the comments section. |
| Recorded WED - Non-Survey Grade GPS | The parcel’s boundary has been constructed from coordinate geometry sourced from the recorded easement deed based on GPS coordinates that do not fit within survey grade tolerances. (Non-Survey Grade GPS, Plugger Survey, Handheld GPS coordinates, etc.) | A reference in the comments section should be made as to the type of GPS used for dada capture. |
| Boundary Data from Entities |
| GIS Parcel Data – City, County, State, or Federal | This method is typically used for boundary data from Entities for Non-stewardship easements. The parcel’s boundary was downloaded by an Entity from GIS digital data taken from a City, County, State, or Federal GIS Department. | Add the name of the source and/or website in the comments. |
| GIS Parcel Data – Other | This method is typically used for boundary data from Entities for Non-stewardship easements. This parcel’s boundary was provided by the Entity from a non-government source, not from a Licensed Professional Surveyor. | Add the name of the source and/or website in the comments. |
| Heads Up Digitized (Non-COGO) |
| Imagery - DOQQ | The parcel’s boundary has been digitized by hand using 1:24,000 scale imagery. | The vintage or currency of the imagery should be provided in the comments section. |
| Imagery - NAIP | The parcel’s boundary has been digitized by hand using the best available NAIP imagery. | The vintage or currency of the imagery should be provided in the comments section. |
| Imagery – Other Hi RES | The parcel’s boundary has been digitized by hand using another imagery source. | The vintage or currency of the imagery should be provided in the comments section. |
| Scale | The map scale at which the boundary was digitized. |
| Comment | Add notes. |
| Data Entry User | Enter your name. |
| Data Entry Date | Fill in this Date |

Legal Survey is a “signed and sealed” field survey plat executed by a professional licensed land surveyor in good standing at the time of execution in the state where the observations occurred.

2 Geographic Position (GP) is a geographical/geospatial point represented by latitude, longitude, and Datum.

3 Shared Data/Alternate Source are data or information originating from a source other than NRCS.  These shared data can originate from other federal government agencies, state government agencies, county government.

Please note for new 2021 Methods: All newly closed easements and re-establishment surveys will have a new 2021 Method of “Legal Survey   - Survey Grade GPS or State Plane Coordinates .”  All easement boundary corrections and easement boundaries from an Entity will have the 2021 Method provided.

A re-established survey/boundary is one that has been conducted to delineate and/or correct an existing survey or that has been conducted to establish a legal survey when a prior survey has not been conducted.

## Topology Check

## The Topology rule of “No Ovelaps” is no longer required. We want to avoid the possibility of corrupting correct easement boundary data. All overlaps will require further investigation and due diligence by EPD for correction of the national easement boundary layer.

MOST Importantly when updating your checkout, any new or modified/updated polygons (geometry and/or attributes) must be copied in to the “ReturnToGEO.gdb” layers (see those highlighted in Blue in the graphic below), which is the only file geodatabase that you need to return to the Fort Worth GEO office.

You have now completed the process and can submit your checkout “ReturnToGEO.gdb” to GEO, Fort Worth, for aggregation into the main database. Please be sure to return your checkout for processing before the due date. Checkouts expire at the close of the quarter and must be submitted before the expiration date.

# Additional Training Materials

## ESRI Virtual Campus

The ESRI Virtual Campus training provides a high-quality learning experience using online-interactive exercises, examples, and instructional resources to create a rich learning environment.

These courses are available at no cost. The courses teach a variety of topics related to ESRI software, the theory underlying GIS technology, and the application of GIS tools in particular fields. Some Web courses include downloadable trial editions of ESRI software. View the list of courses (http://training.esri.com/gateway/index.cfm?fa=aul.premiumCourses).

For ordering information please go to the ESRI Virtual Campus Training web page on the National Employee Development Center course listing located at http://www.nrcs.usda.gov/wps/portal/nrcs/detail/national/nedc/training/gis/?cid=nrcs143_024136